## Slide 1: Immersive Mapping in Virtual Reality for Robot Teleoperation
Rubin Khadka Chhetri (6558048)
Sarvenaz Ashoori (6878764)
Abdul Hayee Hafiz (6029926)

## Slide 2: Problem Statement
2D displays lack depth perception
Poor distance judgment
High mental workload
Inefficient navigation in tight spaces

## Slide 3: Proposed Solution
Immersive VR Visualization
Multi-camera System
Minimap and distance feedback
Cross platform Architecture

## Slide 4: System Architecture

## Slide 5: Mapping & Environment
Point Cloud
Static Mesh

## Slide 7: Robot Movement & Controller Mapping
How Robot Moves
Unity does not move robot directly
Input -> /cmd_vel -> Gazebo -> /odom -> Unity -> VR
Gazebo is single source of truth for physics
Controller Input
Primary: Meta Quest thumbstick
Challenge: Simulator thumbstick emulation unrealiable
Solution: Keyboard Fallback to validate pipeline

## Slide 8: VR Interface Design
Main
Following
Right Wheel
Left Wheel
Multi Camera System

## Slide 9: VR Interface Design
Minimap
Distance Feedback
Communication Health State

## Slide 10: Results & Validation
Topic | Measured Rate | Expected Max
/cmd_vel | 71-72 Hz | ~72 Hz
/odom | 47-48 Hz | 50 Hz
/scan | 9-10 Hz | 10 Hz

## Slide 11: Result & Validation

## Slide 12: Challenges & Future Direction
Challenges
WiFi unreliable -> Ethernet + static IP
DirectX11 crashes -> Switched to Vulkan
Future Direction
Industrial WiFi/ 5G
Physical Hardware Testing
Live SLAM for unmapped environments
🔗 All code and assets: github.com/rubin-khadka/VR_Controlled_Robot_Teleop